To develop the software, I used the STM32H743ZIT6 microcontroller. First, I started by modifying the .ioc file, enabling the SPI interface in FULL-DUPLEX MASTER mode.
For the microcontroller's GPIOs, I used:
- PA4 for Chip Select;
- PA8 (input) for the BUSY bit (bit 1 of the status register);
- PA9 (output) for the HW and SW reset command;

## Configuration of L6470 Driver
I began developing the driver by creating the header file l6470_driver.h, where I defined the software interface to control the L6470 chip via SPI communication.
Within the header, I included two main structures:
- L6470_Config_t: Hardware configuration
  - SPI interface to use.
  - GPIO pins for control (Chip Select, Reset, Busy, Standby).
  - DMA management parameters.
- L6470_Handle_t: Driver handle
  - Contains the motor's configuration and operational parameters.
And the prototypes of the functions to be implemented in the l6470_driver.c file:
- L6470_Init(): Driver initialization (copies HW configuration, sets default parameters).
- L6470_GoTo(): Absolute movement to a position.
- L6470_SendCommand() - Sends single commands L6470_SendData() / L6470_ReceiveData() (Using the HAL_SPI_TransmitReceive function provided for communication with the module).
- L6470_SetParam() / L6470_GetParam(): Parameter configuration.
I implemented these prototypes in the l6470_driver.c file.
I assumed the use of a generic 200-step-per-revolution Stepper Motor in microstepping mode, setting the following configuration parameters (Section //Set default parameters in main.c): the step mode to 1/16. This means the motor performs 16 micro-steps to complete a single full step, guaranteeing 3200 microsteps/revolution.
For speed, I set a value of 1600, achieving a precise half-turn in 1 second. For acceleration, not knowing the type of load attached to the motor, I maintained an acceleration/deceleration of 100 steps per second squared, aiming to ensure a sufficiently smooth movement without losing steps.

## Movement Function
Besides the initialization, motor status reading, and current position functions, I would describe the movement function:
//Function for precise half-turn movement (with error control)
status_move = L6470_PreciseMove(&hstepper, t_position, timeout, tolerance);
Before calling this function in main, I perform a hardware and software reset of the motor to return it to its default position: L6470_ResetPosition(&hstepper);.
At the beginning of the function, I wait for the change of state of the BUSY bit, passing it a timeout in milliseconds: L6470_WaitWhileBusy(hmotor, timeout_ms). Once the timeout expires, if the BUSY bit is still high, it returns a timeout status to be managed with a TODO (perhaps logging a failure detailing the cause of the timeout).
If, on the other hand, it returns an OK status, I execute the GoTo command: L6470_GoTo(hmotor, target_position);, immediately calculating the motor's position to check the current position.
Afterward, I planned the implementation of the following while loop:
while (abs(current_pos - target_position) > tolerance && (HAL_GetTick() - start_time) <= timeout_ms) { // Tolerance of 5 microstep
    L6470_GoTo(hmotor, target_position);
    //I will try to correct by recalculating the position
    current_pos = L6470_GetPosition(hmotor);}
Where:
- current_pos = L6470_GetPosition(hmotor);: Immediately after sending the GoTo command, the function reads the motor's current position.
- while (abs(current_pos - target_position) > tolerance && (HAL_GetTick() - start_time) <= timeout_ms): This is the correction and verification loop. The loop continues as long as:
  - The absolute difference between current_pos and target_position is greater than tolerance. This means the motor has not yet reached the desired position with the required precision.
  - The timeout_ms from the start of the function has not expired.
- L6470_GoTo(hmotor, target_position);: This is the key point and potential criticality. Continuous re-sending of GoTo: If the motor is very close to the position but not exactly within tolerance, and especially if the tolerance is very small, the while loop could continue to send L6470_GoTo commands repeatedly. This could generate "jerky" movement of the motor as it approaches the final position, since each GoTo restarts the movement profile (acceleration, steady speed, deceleration). If the motor is not yet in the correct position (within tolerance), the function sends the GoTo command to the target_position again. The idea is to "recall" the motor to the desired position, in case it lost steps or did not reach the precise destination on the first attempt.
- current_pos = L6470_GetPosition(hmotor);: The position is re-read after the new GoTo command for the next iteration of the loop.

## DMA Management and Callbacks
In the program, I also included DMA management for SPI transmission. I created ad-hoc functions for transmitting/receiving information via DMA, setting Stream 1 (Mem to Peripheral) for TX and Stream 0 (Peripheral to Mem) for RX.
I also override the Callback functions for managing the wait after the transmission command in the L6470_SendCommand_Data_DMA function, triggering on the bits hstepper.config.transfer_complete = true; and hstepper.config.transfer_error = true;.

## Future Implementations
One could consider implementing functions to gradually disable the drivers (high impedance) or to immediately disable the drivers.